## Slide 1: Hot Side Oxidation (HSO)
Ricardo Fritzsche, Ph.D.

## Slide 2: Shout-out / Thanks
German Brewing Forum
Reviewers
CT Owen
Techbräu
Matt Chrispen
Bryan Rabe
Jeff Rankert
Nico
Abbey (CT)
Notes: This presentation will cover
What is HSO and where it fits
The evidence for HSO (or not)
Narziss pilot experiments
Conclusions from the scientists
What can you do to minimize HSO
Antioxidants and HSO
How to design your own HSO experiment
Can you taste the difference?

## Slide 3: Introduction
What is HSO and where it fits
The evidence for HSO (or not)
Conclusions from the scientists
Narziss pilot experiments
What can you do to minimize HSO
How to design your own HSO experiment
Can you taste the difference?
Antioxidants and HSO
Notes: This presentation will cover
What is HSO and where it fits
The evidence for HSO (or not)
Narziss pilot experiments
Conclusions from the scientists
What can you do to minimize HSO
Antioxidants and HSO
How to design your own HSO experiment
Can you taste the difference?

## Slide 4: What is HSO and where it fits
Notes: Introduction
Hot side oxidation, aka HSA is one of today’s hottest topics
Avoiding it is part of the LO brewing aka LODO brewing process
You can type low oxygen brewing in Google and it will direct you to several recent references on the topic
Relatively new to brewing – this may be new to you or you probably read/ heard that HSA or HSO is a myth or you read/ heard about LODO.
Relatively old to brewing – You may have heard or read about George Fix, one of the first homebrew celebrities, and the one that popularized the HSA concept among homebrewers (before it became a myth)
Truth is that it is that it has kept the brewing community interested for many years, and that many major centers of brewing research have worked on the problem.
All German manufactures I know presently manufacture equipment modified to apply low oxygen techniques, and there are many commercial products designed to either control HSO or to deal with the byproducts of HSO via finings.
The interest in oxidation during the mash started in the 70s. At the time, has been known for many years that oxidation was bad for beer and staling molecules like trans-2-nonenal had already been identified.
In 1975, Hashimoto’s finding that the increase in t-2-nonenal was unrelated to bottle oxidation led to many experiments on hot side oxidation; unfortunately many of them did not provide any organoleptic data.
I will now present most of the organoleptic data available to us with additional data for historical context.

## Slide 5: What is Hot Side Oxidation
It is the introduction of oxygen in the form of air in any of the hot-side brewing processes
Introduction/ transfer of liquids/ solids
Mashing
Rinsing – Lautering
Boiling (including heating and cooling)
Notes: Definition of HSO

## Slide 6: Why can HSO be bad?
Gresser, A. – Stability of Beer – C.16 Handbook of Brewing, H. M. Esslinger (ed.), 2009
Transport storage conditions
Time, temperature, light
Barley
Variety, cultivar, harvest year
Vessels
Capacity
Malting
Moisture, O2, kilning
Mashing
Temperature, O2, pH
Milling
Filling
O2
Beer filtration
Primary fermentation
Temperature
Cold break separation
Flotation, filtration, sedimentation
Yeast
Pitching rate, vitality
Wort boiling
Temperature, time, evaporation
Lautering, mash filtration
Hops
Polyphenols
Whirlpool
Time at high temperature
Flavor Stability
Notes: A summary of some factors influencing beer quality in comparison with the initial beer flavor is shown in this figure.

## Slide 7: Brief Timeline
Oxygen discovered in late 1700s
Food and beer oxidation already studied in the 1800s
Beer oxidation state Indicator Time Test published in 1939
In the late 60s and early 70s many papers focused on the role of one of the main villains in beer history, the famous trans-2-nonenal; the culprit of the cardboard flavor in beer: Jamieson 1970, Meilgaard 1971, Visser 1971
In 1975, Hashimoto reported that the formation of nonenal precursors could be traced all the way to lipid oxidation in the mash, and HSO was “born”
Jean DeClerck described oxidation experiments in his 1957 textbook
Notes: Beer and oxidation - timeline

## Slide 8: Some phrases on Hot Side Oxidation
“...some believe that oxygen ingress throughout brewing is important whereas others have concluded that air uptake upstream of the fermenter is an irrelevance.”
Bamforth, C. (2011) J. Inst. Brew. 117, 488-497​
“Hot-side aeration is fundamentally different because of the speed of the redox reactions that occur at elevated temperatures. For example, introducing 1mL of oxygen per liter of wort at 70ºC will start reactions that consume the free oxygen in seconds.”
Fix, G. (1999) Principles of Brewing Science, pp. 130
“That desire to avoid … harshness is what led me to the technique of adding the dark grains during the vorlauf instead of during the mash.”
Strong, G. (2015) Modern Homebrew Recipes, Chapter 6
“In practice air uptake (during mashing) is shown by darker wort and beer color, a less refined beer flavor, and a decreased flavor stability”
Künze, W. (2014) Technology Brewing and Malting, pp.253, English Ed.
Notes: No extra comments

## Slide 9: It’s all ‘bout the mash
MASHING
ADAPTED from Künze, W. Technology Brewing and Malting, Chapter 3 (2014, English)
Proteolisis
Malt quality
Milling
Mashing in
Resting
pH
Enzymes
Milling temperature & Grist storage duration
Oxygen uptake
High mashing in temperature
Mashing-in from below
Oxygen uptake
Mash acidification
Proteolitic rest
LOX 45-55ºC
pH 5.0-7.0
Peroxidase
>60ºC
pH 6.2
Polyphenoloxidase
65ºC
pH 6.5-7.0
Lipase 50-65ºC
pH 6.8-7.0
Polyphenol-rich malts
Curing temperatures
Precursors
Oxygen-protected Wet milling
Notes: Describe factors interacting in the mash
LOX
It is the point at which milled grist is mixed with water than the LOX risk is greatest because it is here that substrate concentrations are high enough for LOX and it is not yet destroyed

## Slide 10: Oxidation at mash-in
Künze, W. Technology Brewing and Malting, Chapter 3 (2014, English)
Grist and water gassed with N2
Grist gassed with N2
Water gassed with N2
Control (no gassing)
Grist gassed with O2
Notes: Chemoluminiscence method
Also see Wurzbacher 2011 – Antioxidant activity in beer

## Slide 11: Mash oxidation consequences
Narziß, L. et al (2017) Abriss der Bierbrauerei, 8 Ed., WILEY-VCH
Slows starch degradation
Slows ß-glucan degradation
Decreases protein degradation
Decreases FAN concentration
Decreases polyphenol concentration (especially anthocyanins and tannoids)
Beers are darker, duller and with less stability
Notes: No extra comments

## Slide 12: Bamforth on hypothesized risks
Temperature regime
Low mashing temp. allow more LOX survival
Heat damage during decoction mashing
Number of vessels
Increased risk of oxygen pick up with more vessels –-for example in decoction mashing--
Oxygen
Oxygen is a substrate for LOX, but also reacting non-enzymatically with –SH groups in proteins to make peroxides, which act as substrates for POD. Also oxygen radical formation
pH
Lower mashing pH reduces rate of LOX; however, superoxide radical more damaging in protonated forms at lower pH
Vessel fabric
Leaching of Cu from copper vessels and chillers; Cu promotes oxygen radical formation
The flavor instability of beer – in Beer, a quality perspective, Bamforth 2009
Notes: Mash oxidation risks per Bamforth

## Slide 13: Künze on hypothesized risks
Künze, W. (2014) Technology Brewing and Malting, 5th ed., VLB Berlin
Conditioned milling (water up to 80ºC)
De-oxygenated mash-in water (boil and chill)
Avoid addition of oxygen during mashing-in; short mash-in time
Keep oxygen away during mashing (nitrogen blanket)
High mashing-in temperature (60-62ºC)
Mash pH under 5.4 (optimal 5.2) from mashing-in onwards
Use biological lactic acid (sauergut)
Gentle mixing of the mash avoiding shear forces
Mashing-out from underneath
No hose elbows – no air in hoses
Phenol-rich malt provides oxidative protection and improves antioxidative potential
Notes: Mash oxidations risks per Künze

## Slide 14: Show me the data! The evidence for HSO
Notes: Well, we have seen the hypotheses but what does the data say?
Hot side oxidation is one of today’s hottest topics and may be new to many of you but reality is that it has kept the brewing community interested for many years, and that many major centers of brewing research have worked on the problem.
The interest in oxidation during the mash started in the 70s. At the time, has been known for many years that oxidation was bad for beer and staling molecules like trans-2-nonenal had already been identified. As I mentioned before, the research Hashimoto published in 1975 let to many experiments on hot side oxidation; unfortunately many of them did not provide any organoleptic data.
I will now present most of the organoleptic data available to us with additional data for historical context.

## Slide 15: First experiments – Lie and Vermiere
Sulfites experiments by Lie in 1977 and Vermiere in 1981 demonstrated oxygen consumptions of 60-200 ppm during the mash
Incidentally, in his most recent book, Narziss states that oxygen consumption in well controlled mashes is around 30-40ppm (but can reach 200ppm in some systems)
Notes: First experiments

## Slide 16: First experiments – Van den Berg / Van Eerde
In 1982, Van den Berg and Van Eerde performed “LODO” experiments using 50 ppm of sulfites in the mash reported better flavor and flavor stability
Notes: As reported by Meilgaard (2001)

## Slide 17: First experiments – Stroh Brewery
Also in 1982, unpublished results of the Stroh Brewery in commercial systems contradicted the above findings, stating that low-oxygen from milling to boil did not show any difference vs control in a series of over 100 sensory comparisons at different ages by a large, trained panel
Notes: As per Meilgaard 2001.

## Slide 18: Aeration during mashing and taste
 | Control | Air | Nitrogen |  | Nitrogen except during |  |  | 
VARIABLES | Control | Air | Conti nuous | Mash-in | Aeration 50°C 30 min | Aeration 65°C 30 min | Aeration 70°C 60 min | Aeration 76°C 8 min
Fresh beer |  |  |  |  |  |  |  | 
Aroma | clean | astring. | clean | clean | slightly husky | slightly husky | slightly husky | clean
Taste | clean | slightly astring. | clean | clean | slightly husky | slightly husky | slightly husky | clean
Body | full | full | full, smooth | full | full | full | full | full
Liveliness | good | moderate | good | good | moderate | moderate | moderate | moderate
Bitterness | good | harsh | good | good | harsh | harsh | medium harsh | slightly harsh
Aged beer (4w. 20°C) |  |  |  |  |  |  |  | 
Aroma | strongly oxidized | strongly oxidized | clean | slightly oxidized | moder. oxidized | moder. oxidized | oxidized | moder. oxidized
Taste | strongly oxidized | strongly oxidized | clean | slightly oxidized | moder. oxidized | moder. oxidized | oxidized | moder. oxidized
Body | full | moder. full | full | full | full | full | full | moder. oxidized
Liveliness | good | less lively | good | good | moder. | moder. | moder. | moder.
Bitterness | slightly harsh | ver.harsh strange | good | good | harsh | harsh | harsh | harsh
Notes: In his 1986 review, Narziss published experiments comparing control to oxygen and nitrogen treatments and reported that continuous and mash-in nitrogen was better than control which in turn was better than air flushing.

## Slide 19: Levels of aeration and taste
Aeration O2 Content mg/L | 0.2 | 2.0 | 3.0 | 10.0
Taste Fresh beer |  |  |  | 
Average DLG | 4.4 | 4.3 | 4.2 | 3.7
Bitterness | 4.2 | 3.5 | 3.2 | 2.3
Test Aged beer |  |  |  | 
Average DLG | 4.0 | 3.5 | - | -
Bitterness | 4.0 | 3.0 | - | -
Narziss, L. Technological factors of flavor stability. J. Inst. Brew. Jul-Aug 1986, Vol. 92, pp. 346
Notes: In a second experiment described in his 1986 review, Narziss Weihenstephan colleagues flushed air at different rates to vary the oxygen content progressively affected taste.

## Slide 20: Levels of aeration and taste
Narziss, L. Technological factors of flavor stability. J. Inst. Brew. Jul-Aug 1986, Vol. 92, pp. 346
O2 Content mg/L | 0.2 | 2.0 | 3.0 | 10.0
pH | 4.40 | 4.40 | 4.41 | 4.41
Color EBC | 5.5 | 6.0 | 7.0 | 8.0
Polyphenols mg/L 12% | 188 | 190 | 187 | 191
Anthocyanins mg/L 12% | 66 | 61 | 50 | 41
Polyphenol index | 2.8 | 3.1 | 3.7 | 4.6
Tannoids mg/L 12% | 58 | 56 | 49 | 42
Total-N mg/100mL 12% | 78 | 78 | 78 | 80
High mol. N mg/100 mL 12% | 14.0 | 13.8 | 13.5 | 14.2
Coag. N mg/100mL 12% | 2.2 | 2.1 | 2.3 | 2.4
Bitter substances EBC | 28.8 | 28.8 | 28.8 | 29.0
Alpha-acids mg/L | 2.0 | 2.2 | 2.5 | 2.3
Iso-alpha-acids mg/L | 28.9 | 29.1 | 28.1 | 27.6
Foam (Ross & Clark) | 121 | 122 | 121 | 121
Alcohol Chilling Test (Chapon) | 3.1 | 4.2 | 5.8 | 9.6
Notes: Wort tannoids are defined as the fraction of polyphenolic compounds which are capable of forming insoluble complexes with proteins. Tannoids include the low and medium molecular polyphenols, the polymers of catechin and anthocyanins. They come from the malt and hops. Although present at relatively low concentration, they play an important part in the colloidal and taste stability of beers. On the one hand they can precipitate the sensitive proteins of the wort and beer, on the other hand they act as protective agents. The tannoid content of beer, wort, barley, malt and hop extracts can be determined by precipitation with polyvinylpyrrolidone (PVP). This polymer which can be considered as a structural analog of proteins binds with tannoids by hydrogen bonding to give an insoluble complex which leads to the formation of a haze. On continuous injection of a solution of PVP into the sample a haze develops until all the tannoids are bound. Beyond this point an excess of PVP brings about a progressive dissolution of the haze.
Alcohol Chilling Test from Chapon (J. Inst. Brew., 1993)
The haze stability is estimated by measuring the haze increase after the addition of alcohol and chilling. The addition of alcohol, to 6% (vol/vol), in beer decreases the solubility of the protein-polyphenol complexes and increases the chill-haze. The beer temperature is lowered to -8°C and the chill-haze is forced out within a total rest time of 40 minutes. The lower the chill-haze the greater the colloidal stability. The chill-haze estimated is principally the protein fraction.

## Slide 21: Carlton brewing experiments
Ageing time (wks.) | Normalized rank sums and significance per Friedman's test |  |  | 
 | Testers | Control 2°C | Control 30°C | Low O2 30°C
0 | 15 | - | 2.4 | 1.8
2 | 11 | 2.5 | 2.7 | 2.4
3 | 12 | 1.6 | 2.5 | 3.2
4 | 11 | 2.1 | 2.5 | 2.5
6 | 12 | 2.0 | 2.9 | 3.0
8 | 10 | 2.1 | 3.0 | 2.8
12 | 9 | 1.9 | 2.7 | 2.9
Average | 11 | 2.0 | 2.7 | 2.7
A high Rank sum means a higher level of staleness
Notes: Per Meilgaard, M (2001) J. Inst. Brew. 107, 271–286
A 1990 investigation at Carlton & United Breweries in Melbourne reported little advantage from low oxygen brewing (i.e., evacuating air from grist, prefilling vessels with nitrogen and deaerating water for mash and sparge). Beers were given staleness scores from 1 (less) to 4 (more). This table shows the average ranks per treatment at the different time points. Of note is that they did report a negative effect of wort aeration (exaggerated HSA).

## Slide 22: Courage brewing experiments
 | Low O2 n=3 | Normal n=3
Runoff, mins. | 103 ± 4.8 | 115 ± 2.0
Last runnings | 1010 ± 1.2 | 1014 ± 1.2
Extract recovery, % | 98.7 ± 2 | 93.7 ± 1.2
HRV Rudin, mins. | 93.3 ± 1.1 | 97.3 ± 0.6
Staleness rating |  | 
Fresh | 0.2 | 0.2
at 2 mo. | 1.2 | 0.7
at 3 mo. | 1.3 | 1.4
Overall rating |  | 
Fresh | 3.7 | 3.6
at 2 mo. | 2.6 | 3.0
at 3 mo. | 2.0 | 2.2
Notes: Per Meilgaard, M (2001) J. Inst. Brew. 107, 271–286
In 1992, O’Rourke set up an experiment in a 20hL system to compare 3 low-oxygen brews to 3 normal brews. They milled, mashed and lautered under nitrogen and the liquor and grist were purged with nitrogen. As it can be observed in this table, there were no relevant differences between the treatments. Interestingly, low-oxygen had a slightly negative effect on foam as determined by the Rudin head retention value (HRV).

## Slide 23: Narziss pilot experiments
Notes: Well, these are the hypotheses but what does the data say?
Hot side oxidation is one of today’s hottest topics and may be new to many of you but reality is that it has kept the brewing community interested for many years, and that many major centers of brewing research have worked on the problem.
The interest in oxidation during the mash started in the 70s. At the time, has been known for many years that oxidation was bad for beer and staling molecules like trans-2-nonenal had already been identified. As I mentioned before, the research Hashimoto published in 1975 let to many experiments on hot side oxidation; unfortunately many of them did not provide any organoleptic data.
I will now present most of the organoleptic data available to us with additional data for historical context.

## Slide 24: Mash aeration – Experimental design
TREATMENTS
Wort 1 Control
Wort 2 N2-bubbling during mashing with 15L/kg malt/hour
Wort 3 Air-O2-bubbling during mashing with 15L/kg malt/hour
Wort 4 N2 bubbling (at the 70°C rest air-O2)
Schedule: 50°C 30 min - 65°C 30 min - 70°C 60 min - 77°C 10 min
pH 5,2 (lactic acid)
55L / 10Kg system (Weihenstephan)
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Notes: In 2000, Narziss and the Weihenstephan group published several pilot experiments on the most common mashing variables. The first experiment explored the effect of gassing a pH 5.2 mash with nitrogen or oxygen.

## Slide 25: Mash aeration – Wort analysis
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Treatment | Sample 1 | Sample 2 | Sample 3 | Sample 4
N2 | NO | YES | NO | Ex 70°C
Air - O2 | NO | NO | YES | Only at 70°C
Wort Color EBC | 6.6 | 6.7 | 9.4 | 7.3
High molecular N mg/100 mL | 23.4 | 22.3 | 24.4 | 23.4
ITT (E 520 nm, 10 Min.) | 0.048 | 0.040 | 0.115 | 0.076
Wort aroma compounds (ppb) |  |  |  | 
3-Methylbutanal | 172 | 110 | 263 | 275
2-Methylbutanal | 42 | 34 | 67 | 67
Benzaldehyde | 7.7 | 4.6 | 11.6 | 11.5
Phenylacetaldehyde | 1469 | 900 | 2157 | 2161
1-Penten-3-ol | 4.8 | Tr. | 9.2 | 10.5
Benzylalcohol | 18.8 | 12.5 | 24.1 | 24.9
Furfural | 375 | 311 | 794 | 784
Notes: DLG test
The quality of the beer, the alcohol content, and the turbidity are determined by the application of the forcing test 0/40 ° C. according to MEBAK. Beer is alternately subjected to temperatures of 40°C. and 0°C. in this method until after the cold treatment a precisely defined turbidity increase or a slight opalescence can be observed. Foam stability is a further important quality feature of beer. The foam index is also included in the 5-point system. The score reached is weighed further by a factor of four, which means that the foam rating is given a great importance in the DLG quality competition with approximately 1/5 of the total score.
Origin of flavor evolution
Hydrolysis of compounds with fresh flavor characteristics: ‘Fresh compounds’ - Mainly esters
Formation of compounds with aged flavor characteristics: ‘Ageing compounds’ - Mainly aldehydes
Result of many chemical reactions
  Oxidative reactions, Maillard reactions, Strecker degradation, furanether formation, release from imine adducts, aldol condensation, β-damascenone formation, degradation of hop bitter acids, hydrolysis of esters
Furfural: An aldehyde of furan. It is a colorless oily liquid with the odor of almonds, which quickly darkens when oxidized.

## Slide 26: Mash aeration – Aroma and Taste
Treatment | Sample 1 |  | Sample 2 |  | Sample 3 |  | Sample 4 | 
N2 | NO |  | YES |  | NO |  | Ex 70ºC | 
Air - O2 | NO |  | NO |  | YES |  | Only 70ºC | 
Aromatics (ppb) | Fresh | Aged | Fresh | Aged | Fresh | Aged | Fresh | Aged
3-Methylbutanal | 13.1 | 19.1 | 13.8 | 21.9 | 14.3 | 25.5 | 17.5 | 25.3
2-Methylbutanal | 9.4 | 14.6 | 11.9 | 12.2 | 12.3 | 18.3 | 15.0 | 14.3
Benzaldehyde | 1.0 | 0.8 | 0.8 | 0.9 | 1.6 | 0.9 | 1.1 | 0.9
2-Phenylacetaldeh. | 20.4 | 30.4 | 18.5 | 23.8 | 26.9 | 39.1 | 23.2 | 45.7
g-Nonalactone | 16.0 | 22.3 | 12.7 | 18.1 | 22.6 | 28.7 | 14.4 | 21.8
Furfural | 8.4 | 87.4 | 7.9 | 69.1 | 8.8 | 110.4 | 8.3 | 109.6
DLG Test | 4.1 | 3.1 | 4.2 | 3.6 | 3.6 | 2.9 | 3.8 | 3.0
Aging Test | 1.0 | 2.1 | 1.0 | 1.6 | 1.3 | 2.5 | 1.0 | 2.6
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Notes: DLG test
The quality of the beer, the alcohol content, and the turbidity are determined by the application of the forcing test 0/40 ° C. according to MEBAK. Beer is alternately subjected to temperatures of 40°C. and 0°C. in this method until after the cold treatment a precisely defined turbidity increase or a slight opalescence can be observed. Foam stability is a further important quality feature of beer. The foam index is also included in the 5-point system. The score reached is weighed further by a factor of four, which means that the foam rating is given a great importance in the DLG quality competition with approximately 1/5 of the total score.

## Slide 27: Mash aeration – Beer analysis
Treatment | Sample 1 | Sample 2 | Sample 3 | Sample 4
N2 | NO | YES | NO | Ex 70ºC
Air - O2 | NO | NO | YES | Only 70ºC
Attenuation % | 81.8 | 83.7 | 83.0 | 82.7
Color EBC | 6.4 | 5.7 | 8.1 | 7.8
pH (end of fermentation) | 4.6 | 4.6 | 4.7 | 4.6
Total-N mg/100mL | 123.0 | 125.0 | 114.0 | 120.0
High molecular N mg/100mL | 21.0 | 18.9 | 20.7 | 20.4
FAN mg/100mL | 24.4 | 25.0 | 21.3 | 23.9
Polyphenols mg/L | 202.0 | 209.0 | 67.0 | 132.0
Foam R&C test | 100.0 | 89.0 | 102.0 | 97.0
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Notes: The change of the wort color is related to the respective oxidation; The degradation of the high molecular weight N (a test for foam stability) is caused by the O2 of the mash, the reducing substances exhibit a higher potential under an inert atmosphere (Sample 2).
Polyphenols / Brewtan effect ?

## Slide 28: Mash-in temperature – Treatments
TREATMENTS
Wort 5: rests of 50, 65, 70, 77°C for 30, 30, 60,10 min, resp.; TMD 157 min
Wort 6: 35, 50, 62, 70, 75°C for 15, 30, 45, 45, 10 min, resp.; TMD 185 min
Wort 7: rests of 50, 62, 70, 75°C for 30, 45, 45, 10 min, resp.; TMD 155 min
Wort 8: rests of 62, 70 and 75°C for 45, 60 and 10 min, resp.; TMD 128 min
pH 5,2 (lactic acid)
55L / 10Kg system (Weihenstephan)
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Notes: The second experiment explored the influence of mashing temperature.

## Slide 29: Mash-in temperature – Aroma and Taste
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Treatment | Sample 5 |  | Sample 6 |  | Sample 7 |  | Sample 8 | 
Mash-in temperature | Std. 50°C |  | 35°C |  | 50°C |  | 62°C | 
Aromatics in ppb | Fresh | Aged | Fresh | Aged | Fresh | Aged | Fresh | Aged
3-Methylbutanal | 10.7 | 14.2 | 10.7 | 15.1 | 10.2 | 12.8 | 10.0 | 12.6
2-Methylbutanal | 6.1 | 7.3 | 6.7 | 8.3 | 4.1 | 7.0 | 7.6 | 8.2
Benzaldehyde | 0.8 | 1.1 | 0.8 | 1.6 | 0.8 | 1.0 | 0.8 | 1.3
2-Phenylacetaldeh. | 23.0 | 38.5 | 20.7 | 39.2 | 18.3 | 32.6 | 22.6 | 41.8
g-Nonalactone | 27.9 | 45.5 | 25.2 | 41.9 | 21.2 | 37.8 | 21.6 | 36.6
Furfural | 8.8 | 77.0 | 9.1 | 110.0 | 8.3 | 99.7 | 6.9 | 84.6
Nicotin acid eth ester | 15.9 | 29.3 | 18.0 | 33.8 | 13.6 | 27.9 | 13.1 | 29.8
DLG Test | 3.4 | 3.2 | 3.8 | 3.3 | 4.0 | 3.2 | 3.6 | 3.0

## Slide 30: Mash-in temperature – Mash analysis
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
VARIABLE | Sample 5 | Sample 6 | Sample 7 | Sample 8
Mash-in temperature | Std. 50°C | 35°C | 50°C | 62°C
Wort Color EBC | 9.8 | 10.7 | 9.0 | 8.7
ITT (E 520 nm, 10 Min.) | 0.223 | 0.225 | 0.265 | 0.297
Wort aroma compounds (ppb) |  |  |  | 
3-Methylbutanal | 107.5 | 148.4 | 131.6 | 96.6
2-Methylbutanal | 57.6 | 52.7 | 52.1 | 41.5
Benzaldehyde | 6.6 | 4.8 | 5.6 | 4.3
Phenylacetaldehyde | 1034 | 894 | 937 | 862
1-Penten-3-ol | 6.6 | 1.4 | 3.0 | 1.0
Benzylalcohol | 22.9 | 17.2 | 18.1 | 13.1
Furfural | 166.3 | 162.0 | 160.0 | 157.3

## Slide 31: Mash-in temperature – Beer analysis
VARIABLE | Sample 5 | Sample 6 | Sample 7 | Sample 8
Mash-in temperature | Std. 50°C | 35°C | 50°C | 62°C
Attenuation % | 83.2 | 82.6 | 82.6 | 82.9
Color EBC | 7.8 | 9.0 | 7.1 | 7.2
pH (end of fermentation) | 4.6 | 4.7 | 4.7 | 4.7
Total-N mg/100mL | 89.7 | 94.5 | 91.3 | 81.4
High molecular N mg/100mL | 17.5 | 17.8 | 16.9 | 15.4
FAN mg/100mL | 15.3 | 17.2 | 16.9 | 13.1
Polyphenols mg/L | 194 | 200 | 172 | 173
Anthocyanins mg/L | 69 | 78 | 80 | 77
Foam R&C test | 126 | 128 | 129 | 125
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204

## Slide 32: Mash pH effect – Treatments
TREATMENTS
Wort 9: pH 5.8 – no acidification
Wort 10: pH 5.5 by addition of lactic acid
Wort 11: pH 5.2 by addition of lactic acid
Wort 12: pH 5.2 (lactic acid), gas O2 15L/kg malt/h
50°C 30 min - 65°C 30 min - 70°C 60 min - 77°C 10 min
55L / 10Kg system (Weihenstephan)
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Notes: The third experiment researched the effect of three different mash pH and oxygen at pH 5.2.

## Slide 33: Mash pH effect – Wort analysis
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Treatments | Sample 9 | Sample 10 | Sample 11 | Sample 12
Different mash-pH | 5.8 | 5.5 | 5.2 | 5.2
Air – O2 | NO | NO | NO | YES
Wort Color EBC | 9.8 | 9.6 | 7.9 | 11.0
ITT (E 520 nm) | 0.203 | 0.213 | 0.226 | 0.426
Wort aroma compounds (ppb) |  |  |  | 
3-Methylbutanal | 127.5 | 135.0 | 143.6 | 178.3
2-Methylbutanal | 81.8 | 65.0 | 77.6 | 80.4
Benzaldehyde | 4.6 | 5.2 | 7.1 | 9.2
Phenylacetaldehyde | 785 | 949 | 1160 | 1511
1-Penten-3-ol | 14.6 | 5.3 | 11.5 | 8.2
Furfural | 126.4 | 229.6 | 364.7 | 563.5
Notes: Origin of flavor evolution
Hydrolysis of compounds with fresh flavor characteristics: ‘Fresh compounds’ - Mainly esters
Formation of compounds with aged flavor characteristics: ‘Ageing compounds’ - Mainly aldehydes
Result of many chemical reactions
  Oxidative reactions, Maillard reactions, Strecker degradation, furanether formation, release from imine adducts, aldol condensation, β-damascenone formation, degradation of hop bitter acids, hydrolysis of esters

## Slide 34: Mash pH effect – Beer analysis
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Treatments | Sample 9 | Sample 10 | Sample 11 | Sample 12
Different mash-pH | 5.8 | 5.5 | 5.2 | 5.2
O2 | NO | NO | NO | YES
Attenuation % | 83.4 | 84.0 | 82.6 | 82.6
Color EBC | 7.3 | 7.0 | 6.8 | 8.2
pH young beer | 4.61 | 4.63 | 4.56 | 4.47
Total N mg/100mL | 87.4 | 109.7 | 117.1 | 113.7
High mol. N mg/100mL | 15.1 | 16.2 | 15.6 | 15.0
FAN mg/100mL | 15.3 | 22.2 | 24.0 | 22.9
Polyphenols mg/L | 198 | 191 | 198 | 92
Anthocyanins mg/L | 82 | 95 | 107 | 37
Foam | 119 | 110 | 101 | 116
ITT (fresh) | 0.220 | 0.182 | 0.175 | 0.275
Alcohol Chilling Test | 36.4 | 19.9 | 18.3 | 9.6
Notes: Alcohol Chilling Test from Chapon (J. Inst. Brew., 1993) The lower the chill-haze the greater the colloidal stability.
The haze stability is estimated by measuring the haze increase after the addition of alcohol and chilling. The addition of alcohol, to 6% (vol/vol), in beer decreases the solubility of the protein-polyphenol complexes and increases the chill-haze. The beer temperature is lowered to -8°C and the chill-haze is forced out within a total rest time of 40 minutes. The lower the chill-haze the greater the colloidal stability. The chill-haze estimated is principally the protein fraction.

## Slide 35: Mash pH effect – Aroma and Taste
Treatment | Sample 9 |  | Sample 10 |  | Sample 11 |  | Sample 12 | 
pH | 5.8 |  | 5.5 |  | 5.2 |  | 5.2 | 
Air O2 | NO |  | NO |  | NO |  | YES | 
Aroma compounds (ppb) | Fresh | Aged | Fresh | Aged | Fresh | Aged | Fresh | Aged
3-Methylbutanal | 9.6 | 14.9 | 14.1 | 19.3 | 13.2 | 18.8 | 13.7 | 21.0
2-Methylbutanal | 5.8 | 9.4 | 6.5 | 9.4 | 5.8 | 8.3 | 6.6 | 9.2
Benzaldehyde | 0.7 | 1.8 | 1.0 | 1.1 | 0.6 | 1.1 | 0.8 | 1.4
Phenylacetaldehyde | 18.3 | 30.7 | 18.7 | 37.2 | 21.8 | 45.6 | 30.4 | 63.4
g-Nonalactone | 27.5 | 42.0 | 25.1 | 41.5 | 30.3 | 47.9 | 41.3 | 60.4
Furfural | 7.7 | 119.6 | 15.2 | 114.0 | 12.8 | 122.3 | 15.4 | 204.4
Ethyl nicotinate | 12.4 | 33.4 | 13.5 | 33.9 | 13.2 | 25.0 | 12.6 | 30.8
Flavor DLG test | 3.2 | 3.2 | 3.8 | 3.2 | 3.8 | 3.7 | 3.4 | 2.8
Aging | 1.1 | 2.0 | 1.0 | 1.9 | 1.0 | 1.4 | 1.4 | 2.8
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Notes: Furfural concentrations rise as beer ages, especially if it has been exposed to heat, and give the amber nectar a musty taste.
Brewers measure furfural and other freshness indicators using techniques such as high performance liquid chromatography (HPLC), but this involves expensive equipment and time-consuming sample preparation.

## Slide 36: Aeration Temperature – Wort
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Treatment | Sample 13 | Sample 14 | Sample 15 | Sample 16
Nitrogen 150L/h | continuous | cont. except | cont. except | cont. except
Aeration 15L/kg/h | none | 50°C | 65°C | 70°C 30 min
Wort Color EBC | 8.9 | 9.0 | 10.8 | 11.7
Total-N mg/100mL | 114.5 | 117.5 | 118.2 | 121.3
High molecular N mg/100mL | 23.7 | 24.4 | 24.5 | 25.7
FAN mg/100mL | 25.7 | 25.3 | 25.0 | 25.6
Polyphenols mg/L | 229 | 200 | 193 | 205
Wort aroma comp. (ppb) |  |  |  | 
3-Methylbutanal | 129.9 | 139.1 | 157.3 | 140.2
2-Methylbutanal | 60.3 | 67.7 | 68.4 | 50.0
Benzaldehyde | 5.1 | 4.6 | 5.4 | 5.7
Phenylacetaldehyde | 937 | 943 | 1205 | 1124
1-Penten-3-ol | 1.6 | 4.1 | 3.4 | 2.0
g-Nonalactone | 3.5 | 3.8 | 4.8 | 5.9
Furfural | 149.6 | 156.7 | 201.4 | 175.6
Notes: The fourth experiment explored the effects of oxygen during different mash rests.
Note the effect of aeration at 70C on wort color

## Slide 37: Aeration Temperature – Beer
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Treatment | Sample 13 | Sample 14 | Sample 15 | Sample 16
Nitrogen 150L/h | continuous | cont. except | cont. except | cont. except
Aeration 15L/kg/h | none | 50°C | 65°C | 70°C 30 min
Attenuation % | 83.8 | 84.0 | 84.4 | 84.1
Color EBC | 7.2 | 7.7 | 8.0 | 7.5
pH young beer | 4.65 | 4.63 | 4.59 | 4.61
Foam (R&C) | 120 | 119 | 125 | 126
ITT (fresh) | 0.118 | 0.142 | 0.163 | 0.187
Alcohol Chilling Test | 37.3 | 32.2 | 28.3 | 36.4
Notes: Alcohol Chilling Test from Chapon (J. Inst. Brew., 1993) The lower the chill-haze the greater the colloidal stability.

## Slide 38: Aeration Temperature – Aroma and Taste
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Treatment | Sample 13 |  | Sample 14 |  | Sample 15 |  | Sample 16 | 
Nitrogen 150L/h | continuous |  | cont. except |  | cont. except |  | cont. except | 
Aeration 15L/kg/h | none |  | 50°C |  | 65°C |  | 70°C 30 min | 
Aroma comp. (ppb) | F | A | F | A | F | A | F | A
3-Methylbutanal | 12.2 | 16.3 | 12.3 | 15.8 | 15.0 | 19.4 | 14.1 | 16.4
2-Methylbutanal | 3.1 | 5.0 | 4.1 | 5.4 | 5.0 | 6.1 | 4.6 | 5.6
Phenylacetaldeh. | 20.4 | 30.5 | 27.4 | 41.5 | 23.4 | 41.4 | 26.2 | 44.5
g-Nonalactone | 29.0 | 36.1 | 32.4 | 44.2 | 26.7 | 41.8 | 29.2 | 48.0
Furfural | 9.9 | 107.7 | 11.0 | 140.9 | 12.2 | 144.6 | 13.1 | 178.1
Nicot ac eth ester | 44.5 | 55.7 | 47.5 | 56.6 | 44.5 | 55.1 | 47.3 | 65.4
Flavor DLG test | 3.9 | 3.5 | 3.7 | 3.6 | 3.8 | 3.2 | 3.8 | 3.2
Aging | 1.0 | 1.8 | 1.0 | 1.8 | 1.0 | 2.2 | 1.1 | 2.0

## Slide 39: Conclusions from the scientists

## Slide 40: Charlie Bamforth
If the effect exists, it is small
Recommends that flavor stability be evaluated organoleptically
Notes: Bamforth, in his 2009 book chapter in flavor stability adds that there has been an over-reliance on chemical and instrument data, and he recommends that flavor stability be evaluated organoleptically. He has repeated this concept in homebrewing podcasts.

## Slide 41: Bamforth on hypothesized risks
Temperature regime
Low mashing temp. allow more LOX survival
Heat damage during decoction mashing
Number of vessels
Increased risk of oxygen pick up with more vessels – for example in decoction mashing
Oxygen
Oxygen is a substrate for LOX, but also reacting non-enzymatically with –SH groups in proteins to make peroxides, which act as substrates for POD. Also oxygen radical formation
pH
Lower mashing pH reduces rate of LOX. However, superoxide radical more damaging in protonated forms at lower pH
Vessel fabric
Leaching of Cu from copper vessels; chillers. Cu promotes oxygen radical formation
The flavor instability of beer – in Beer, a quality perspective, Bamforth 2009

## Slide 42: Ludwig Narziss
Beers are darker, duller and with less stability

## Slide 43: Morten Meilgaard
All experiments showing oxygen taste damage were performed at a lab scale (aka homebrew scale)
Little effect was demonstrated in an industrial scale
WHY? Cube-square law?
Notes: Morten Meilgaard of flavor wheel fame
Meilgaard literature review concluded that all experiments showing damage from oxygen were performed at a lab scale (aka homebrew scale), but that little effect was demonstrated in an industrial scale. Nonetheless, he concluded that there is no harm and that if the equipment makers offer the protection at no extra cost, why not take it, especially in a micro or nanobrewery (he means homebrewing).

## Slide 44: But it only applies to big brewers, right?
Commercial batches can be higher than 100,000 liters (850 bbl)
Brewing scientists do NOT generally run experiments in large-scale commercial systems
It would not make sense
Research is mostly done in pilot breweries, ranging in size from 50 to 500 liters (13 to 130 gallons) and many experiments are done in even smaller systems
It follows that research data is generally more applicable to homebrewers than to professional brewers
as the size of the research systems is more similar to that of homebrewers
1-2 to 1-20 ratio: homebrewers to pilot breweries
1-20 to 1-2000 ratio: pilot to commercial breweries

## Slide 45: What you can do to minimize HSO

## Slide 46: Minimizing HSO
Adapted from Künze, W. (2014) Technology Brewing and Malting, 5th ed., VLB Berlin
Fill kettle / mash tun from the bottom
Keep air away during mashing (cover the mash/ nitrogen blanket)
High mash-in temperature (148ºF / 64ºC or above)
Mash pH under 5.4 (optimal 5.2) from mashing-in onwards
Gentle mixing of the mash (avoiding shear forces)
No splashing / air contact during recirculation
Malt with high content of non-oxidized polyphenols
Malt with no LOX
De-oxygenated mash-in water (boil and chill)
No copper in the hot-side (including chiller)

## Slide 47: Antioxidants and HSO

## Slide 48: Antioxidants and HSO
Bisulfites – Sodium or potassium
Ascorbic acid
Use with other Antioxidants
Gallotanins
Brewtan B, Tannox-Brew, Tan’Activ GTH
Combos
Antioxin SBT
Notes: The major pathways that have been proposed for carbonyl formation are (Kaneda 1991);
Strecker degradation of amino acids,
oxidative degradation of isohumulones,
oxidation of alcohols to aldehydes,
autooxidation of fatty acids,
enzymatic degradation of lipids,
aldol condensation of aldehydes, and
secondary autooxidation of long chained unsaturated aldehydes.
For the antioxidant potential of sulfites, Kunz in 2002 made a very good study tracking the influence of SO2 concentration on oxidative lag time.

## Slide 49: How to design your own HSO experiment

## Slide 50: Designing your own HSO experiment
The ideal 2-treatment experiment changes only one variable
The ideal experiment maximizes the effect of the experimental variable
Beer should be excellent (BJCP 38+ points)

## Slide 51: Designing your own HSO experiment
Pick a subtle, malty style
Brewer must be experienced in the style and very consistent
Pick a style to maximize the odds of finding a difference

## Slide 52: Designing your own HSO experiment
Is your control a good control?
Low O2 water
Malt has no LOX
Mash pH 5.4 to 5.2
Mash in ≥ 148ºF/ 64ºC
Mash cap
No air during recirculation
Gentle mash mixing/ no splashing

## Slide 53: Designing a HSO experiment
Other variables that can affect beer oxidation
Wort is not turbid
Separate hot / cold break
Sufficient/ active/ oxygenated yeast
Low thermal load
“Spunding” or keg-conditioning

## Slide 54: How to measure mash oxidation
Oxygen consumption can be estimated indirectly measuring metabisulfite changes
A validated method is the Iodine titration method (e.g. Hanna 3822 Sulfite Test Kit)
Best breweries consume 30-40 mg O2/L of wort (about 1:1 SMB to O2 per Ilett, 1995)
Some breweries can consume up to 200 mg O2/L wort
A direct determination of the oxygen content of the mash is not possible because of the active oxidase systems (rendering DO meters useless for mashing measurements)
Narziß, L. et al (2017) Abriss der Bierbrauerei, 8 Ed., WILEY-VCH
Notes: Section 2.3.1.8 – Narziss 2017

## Slide 55: Can you taste the difference?

## Slide 56: De gustibus non est disputandum
Guinard and Bamforth have done experiments demonstrating that in certain cases stale beer can be preferred to fresh beer
It is possible that there is a flavor to low-oxygen-mash beer and it is reasonable to assume that it is more prevalent in German beers as modern low-oxygen brewhouses were originally designed in Germany and are more prevalent there
It is unlikely that low-oxygen-mash beers will be proven as better beers – it probably depends on your starting point
Great beer is in the taste of the be(er)holder

## Slide 57: References – 1 of 2
Bamforth, C (2011) J. Inst. Brew. 117, 488-497​
​​Bamforth, C (2014) BeerSmith Podcast, #74
Bamforth, C (2009) BrewStrong Podcast, Jan 26, 2009
Currie, R et al (1990), Proc. Inst. Brew. Austr. & NZ, p.117
DeClerck, J (1962), Cours de Brasserie, 2nd ed., Université de Louvain, p429
Fix, G (1998) Brewing Techniques v6 (6)
Fix, G (1999) Principles of Brewing Science, 2nd ed., Brewers Pub, Boulder
Guinard, J ( 2001) Food Quality and Preference , 12 , p243
Hashimoto, N. and Y. Kuroiwa (1975) Rept. Res. Lab. Kirin Br. 18, p. 1
Hug, H et al & Schur, F (1986) Brauerei-Rundschau 97, p.113 & p. 117
Ilett, D (1995) MBAA Tech Quarterly 32, p.213
Krottenhaller et al (2009) Wort Production, in Handbook of Brewing, Ch. 7
Künze, W. (2014) Technology Brewing and Malting, 5th ed., VLB Berlin
Lie, S et al (1977) EBC Proceedings 16th, Amsterdam, p.235

## Slide 58: References – 2 of 2
​MacFarlane, W (1967) Technical Quarterly, Master Brewers Assoc. Amer., p.239
Malfliet, S (2008) J. Inst. Brew. 114, 180–192
Meilgaard, M(2001) J. Inst. Brew. 107, 271–286
Narziß, L (1986) J. Inst. Brew. 92, 346-353
Narziß, L et al (2000) Monatsschrift für Brauwissenschaft 53, Nr. 11/12, p.204
Narziß, L et al (2017) Abriss der Bierbrauerei, 8 Ed., WILEY-VCH
O’Rourke, T et al (1992), P, Proc. Inst. Brew. Austr. & NZ, p.52
O’Rourke, T (2002) The Brewer International, March, pp. 45-47
Stephenson, W. (2003) J. Inst. Brew. 109, 273–283
VandenBerg, R and VanEerde (1982), P, Proc. Inst. Brew. Austr. & NZ, p.70
Vanderhaegen, B (2007) Food Chemistry 103, 404–412
Vermiere, H (1981) EBC Proceedings 18th, Copenhagen, p.81
Wackerbauer, K et al (2003) Mon. für Brauwissenschaft 56, Nr. 9/10, p.174
Wurzbacher, M. (2011) Diss. Technische Universität München

## Slide 59
ANY QUESTIONS?

## Slide 60: HIDDEN SLIDES

## Slide 61: Mash aeration - staling components
Narziss, L. Brewing Science 53, No 11/12, 204-216, 2000

## Slide 62: MASH pH and staling components
Narziss, L. Brewing Science 53, No 11/12, 204-216, 2000

## Slide 63: Influence of hot wort rest in the whirlpool on flavor stability
August Gresser – Stability of Beer – C.16 of Handbook of Brewing, H. M. Esslinger (ed.), 2009
Notes: Fig 16.17 Handbook of Brewing - Lustig , S. ( 1994 ) Das Verhalten flüchtiger Aromastoffe bei der Lagerung von Flaschenbier und deren technologische Beeinfl ussung beim Brauprozeß, Dissertation, TU München.

## Slide 64: Mash-in temperature and flavor stability of beer
Narziss, L. Brewing Science 53, No 11/12, 204-216, 2000
Notes: 16.1.5.3.3 Temperature During the Mashing Process At higher mashing - in temperatures the activity of proteolytic enzymes is reduced. This results in higher amounts of high molecular proteins and better foam properties of the beers. Furthermore, there are lower quantities of amino acids, which cause a minor formation of Maillard products. Thus, a better flavor stability is achieved
Pilot trials on the influence of the various mash parameters on the properties of wort and beer with particular respect to flavor stability. Narziß, L., Back, W., Miedaner, H., and Takahashi, Y.Monatsschrift für Brauwissenschaft 53, No 11/12, 204-216, 2000
Takahashi , Y. ( 1996 ) Pilotversuche über den Einfluß der verschiedenen Maischparameter auf die Eigenschaften der Würze und des Bieres unter besonderer Berücksichtigung der Geschmacksstabilität, Dissertation, TU München .

## Slide 65: Formation of staling flavor
August Gresser – Stability of Beer – C.16 of Handbook of Brewing, H. M. Esslinger (ed.), 2009
Notes: Fig 16.3 Handbook of Brewing - Dalgliesh , C.E. ( 1977 ) Flavor stability, in Proceedings of the 16th European Brewery Convention Congress, Amsterdam , pp. 623 – 59

## Slide 66: Flavor stability of beer
Dalgliesh , C.E. ( 1977 ) Proc. of the 16th European Brewery Convention Congress, Amsterdam , pp. 623
Notes: Fig 15.3 Handbook of Brewing - Dalgliesh , C.E. ( 1977 ) Flavor stability, in Proceedings of the 16th European Brewery Convention Congress, Amsterdam , pp. 623 – 59

## Slide 67: How oxidation works
The flavor instability of beer – in Beer, a quality perspective, Bamforth 2009
Notes: HIDDEN
Bamforth and Parsons (1985) first drew attention to the role of active oxygen species rather than ground-state oxygen in potentiating flavor damage in beer. The principle basis for the toxicity of oxygen is via its conversion to reactive “ free radical ” forms, or reactive oxygen species (ROS) as they are often now collectively termed, because not all damaging species produced from oxygen are radicals.
A free radical is a species with an independent existence containing one or more unpaired electrons. Free radicals can be formed either by loss or acquisition
of electrons from non-radicals. An input of energy to the oxygen molecule can “ flip ” the spin of one of the outer orbital electrons in oxygen, generating the highly reactive singlet oxygen .
Addition of one extra electron to ground-state oxygen forms the superoxide radical, O2– . As superoxide needs to gain only one electron to complete its outermost orbital, it is more reactive than ground state oxygen. One further electron leads to peroxide , O22– , which is not a radical, but is more reactive than ground state oxygen. Essentially the two atoms in the ground state oxygen are held together by two bonds, in superoxide by one-and-a-half bonds and in peroxide by only one bond. This makes the bond in hydrogen peroxide relatively fissile and the input of energy (e.g. as light) effects a splitting.

## Slide 68: Aeration during mashing and taste
 | Control | Air | Nitrogen |  | Nitrogen except during |  |  | 
VARIABLES |  |  | Conti nuous | mash-in | Aeration 50°C 30 min | Aeration 65°C 30 min | Aeration 70°C 60 min | Aeration 76°C 8 min
Wort tannoids mg PVP/L 12% | 89 | 38 | 94 | 92 | 75 | 81 | 55 | 80
Beer stability 0/40/0°C days | 2.1 | 2.5 | 2.1 | 2.1 | 1.6 | 1.8 | 1.7 | 0.9
Alcohol Chilling Test EBC | 17 | 22 | 21 | 20 | 56 | 50 | 54 | 58
Foam (Ross & Clark) | 129 | 128 | 126 | 128 | 126 | 128 | 128 | 128
Narziss, L. Technological factors of flavor stability. J. Inst. Brew. Jul-Aug 1986, Vol. 92, pp. 346
Notes: Hidden slide

## Slide 69: Definitions – Polyphenols and Tannins
Polyphenols are a structural class of organic chemicals characterized by the presence of large multiples of phenol structural units
Tannins are a type of polyphenols that binds to and precipitates proteins and various other organic compounds including amino acids
Tannins have molecular weights ranging from 500 to over 3,000 (gallotannins) and up to 20,000 (proanthocyanidins)
Tannins and many non-tannin polyphenols have antioxidant properties, but it is not yet definitely clear whether these properties protect worts and/or beers from oxidation

## Slide 70: Nonoxidative Mechanism for Development of t-2-Nonenal in Beer
G. Lermusieau, S. Noël, C. Liégeois, and S. Collin
J. Am. Soc. Brew. Chem. 57(1):29-33, 1999
Oxidation is usually recognized as the major cause of development of a stale flavor in beer. However, no significant difference in trans-2-nonenal concentration has been observed between oxygen-receiving and oxygen-free beers after aging. Moreover, (^18)O(2) was not incorporated into the carbonyl fraction, indicating that the cardboard flavor in beer is not due to lipid oxidation in the bottle. As shown by adding deuterated nonenol to the pitching wort, nonenal oxidation and sulfitic adduct degradation were also inefficient pathways oftrans-2-nonenal synthesis. On the other hand, wort nonenal linked to amino acids and proteins revealed to be able to release nonenal at the beer pH. The measured nonenal potential proved a good indicator of beer staling; therefore, UV spectroscopy was used to find which experimental conditions destabilize trans-2-nonenal precursors in wort. Laboratory-scale experiments confirmed that SO(2) can reduce both lipid autoxidation and the nonenal potential rise while the wort is boiling.

## Slide 71: Malt: its role in oxidation
Cantrell, I.C. and Griggs, D.L.
Tech. Q. Master Brew. Assoc. Am., 1996, 33(2), 82-86.
The influence of the composition and properties of malt on the flavour stability of the beer brewed from it is discussed. Topics covered include the enzymic oxidation of malt lipid precursors, leading to the formation of flavour active substances (e.g. the "cardboard" off flavour compound trans-2-nonenal), the possible influence of sulphur compounds in barley on malt and wort quality, the conflicting evidence on the effects of malt polyphenols, the contribution of dimethyl sulphoxide (formed from dimethyl sulphide during malt kilning and turned back into dimethyl sulphide during fermentation) to the total dimethyl sulphide content of the beer, and the formation of reducing agents (which help to delay the onset of the oxidative reactions by which various beer off flavour compounds are formed) during the kilning and/or roasting of different types of malt, especially the darker coloured types.